## Slide 1
Octal Graph Representation for
Multi-Resolution 3D Landform Maps Goro Akagi Yozou Miyadera Tomoe Motohashi
(Nihon Univ.) (Tokyo Gakugei Univ.) (Kanto Gakuin Univ.) Kenshi Nomaki Kensei Tsuchida Takeo Yaku
(Nihon Univ.) (Toyo Univ.) (Nihon Univ.) SIAM Conf. Geometric Design & Comput. Nov.3, 2005 Phoenix, Arizona, USA
1
Notes: Thank you Mr. Chairman.
Today, I'm going to talk about octal graph representation for multi-resolution 3D landform maps.

## Slide 2
1. Introduction
2
Notes: Let me introduce the problems, background, motivation, and purpose of this research.

## Slide 3
1.1 TARGET
3D Landform Maps : 3D computer graphic of
landform.
We employ VRML for 3D landform maps.
altitude
3
we focus on the grid appearing here.
Notes: I will first discuss 3D landform maps.
3D landform maps (3dlms) are 3D Computer Graphic of landform.
We employ VRML for 3D landform maps.
This (right-down picture) shows the basic idea of representation of 3dlms.
This (line of grid) lenghth is the altitude at this point.
3dlms are generated by a great number of altitude data.
In this talk, we focus on the grid appearing here.

## Slide 4
3D Landform Maps
Computation time for rendering and transforming 3D Landform Maps depends on the amount of polygons.
We need to decrease the amount of polygons with keeping its appearance.
Example.
One may need fine (e.g., 50m) meshes in certain focused area, and somewhat rough (e.g., 1km) meshes in other area.
4
Notes: The computation time for rendering and transforming 3dlm depends on the number of polygons.
Therefore, we need to decrease the number of polygons with consisting of 3D objects keeping their appearance.
For example, one may need fine meshes in certain focused areas, and need rather rough meshes in other areas.

## Slide 5
3D landform maps and
Rectangular Dissection
A 3D landform map
This point corresponds to fine mesh of rectangular
dissection.
This point corresponds to rough
mesh of rectangular dissection.
5
  The corresponding rectangular dissection
  Perimeter cell
Notes: To this end, to achieve this, we need rectangular dissections (rd) with 3dlm.
This 3dml corresponds to this Rd.
We note that the perimeter cells of the rectangular dissection are not displayed in this 3dlm.

## Slide 6
1.2 BACKGROUND
Representation of Rectangular Dissection
QuadTree ( Bentley, 1975 )
Rectangular Dual ( kozminski & kinne.1985 )
Octal Degree Rectangular Dissection Graph
( Motohashi et al.2003 ) employ here.
6
We employ Rectangular Dissections to represent 3D Landform Maps.
Notes: As for our background for this work.
Three sets of results were obtained for Rds.
The first was QuadTree obtained by Bentley.
The second was rectangular dual obtained by Kozminski and Kinne.
The third was the Octal degree rectangular dissection graph proposed by our collaborators,
Mr. Yaku, Mr. Tsuchida, and Ms. Motohashi.
We employed the octal degree rectangular dissection graph in this research.

## Slide 7
There are a couple of deficiencies in frequently used operations for rectangular dissection corresponding to multi-resolution 3D landform maps.
(1) unification of cells by quadtree.
(2) computation time of unify-cells by rectangular
dual.
We design a system rendering and transforming 3D Landform Maps, by using octal degree rectangular dissection graphs .
1. 3 MOTIVATION
7
Notes: I will now discuss our motivation for this work.
There are a couple of deficiencies with frequently used operations for rectangular dissection corresponding to multi-representation 3D landform maps at present.
The first is the unification of cells by QuadTree.
The second is the computation time to unify cells by rectangular dual.
Therefore, We design a system rendering and transforming 3D Landform Maps, by using octal degree rectangular dissection graphs .

## Slide 8
1.4 Purpose and Results
Purpose 1 :
To propose a new data structure for
multi-resolution 3D landform maps.
More effective for dynamical changes
of resolutions.
Result 1-1:
We introduce landform octal graph (Sec. 3).
Result 1-2:
We propose a data format named H7-Code for landform octal graphs (sec. 4).
8
Notes: We will now discuss the purpose of our research and the results we obtained.
Our first purpose was to develop a new data structure for multi-resolution 3D landform maps to obtain more effective for dynamical changes in resolutions.
This shows our first result involved the landform octal graph.
This shows our second result involved the H7-code.

## Slide 9
Purpose 2 :
To implement a system rendering and transforming 3D Landform Maps using landform octal graph.
Result 2 :
We design and partially implement system of rendering and transforming 3D Landform Maps (sec. 4).
9
Notes: Our second purpose is to implement a system rendering and transforming for
3D Landform Maps using landform octal graph.
We will design and partially implement system of rendering and transforming 3D Landform Maps (sec. 4).

## Slide 10
Purpose 3 :
To show advantages of our new data
structure.
Result 3 :
We compare the number of meshes reduced by quadtree with that reduced by landform octal graphs (sec. 5).
10
Notes: Our third purpose is to show advantages of our new data structure.
We will compare the number of meshes reduce by quadtree with that by landform octal graph.
(sect. 5)

## Slide 11
2. Preliminaries
11
Notes: Next, let me discuss some preliminaries.

## Slide 12
d
c
Definition
D = (T, P, g) : a rectangular dissection ,
The octal degree rectangular dissection graph
GD=(V, E, L, λ, A, α) for D is defined as follows:
(1) V : (the set of vertexes)
We put a node corresponding to each cell.
D V
12
Notes: The octal degree rectangular dissection is defined as follows.
This is an octal graph corresponding to this rectangular dissection.
First, we define the set of vertexes denoted by V.
We put a node corresponding to each cell.

## Slide 13
（2）E : (the set of edge),λ : E → A : (label function)
  D E λ(e)
c
d
c
d
c
d
c
d
North wall
edge
South Wall
Edge
East Wall
Edge
West Wall
Edge
    nw(c)
    = nw(d)
    sw(c)
    = sw(d)
    ew(c)
    = ew(d)
    ww(c)
    = ww(d)
13
e
e
e
e
Notes: Second, we define the set of edges denoted by E and the label function λ as follows.
If there are no such cells between c and d, then we set an edge denoted by e between their corresponding to nodes.
The label of this edge is the north wall edge.
The south wall edge, east wall edge, and west wall edge are similarly defined.
The south wall edges and west wall edges have been represented by the dotted red line instead of labels.

## Slide 14
（3） A : (the set of the attributes)
α : V → A : (attribute function)
D G
c
2 6
1
2
α(vc)=(1,2,6,2)
nw(c)=1 sw(c)=2
ew(c)=6 ww(c)=2
14
vc
we set an attribute to the corresponding node vc is the 4-tuple (1, 2, 6, 2).
Notes: Third, we define the attribute function, α from V to the set of attributes A.
If the cell c has north wall 1, south wall 2, east wall 6, and west wall 2,
then we set an attribute to the corresponding node vc is the 4-tuple (1, 2, 6, 2).

## Slide 15
Example of Octal degree Rectangular Dissection Graph
Rectangular
dissection
15
Corresponding octal rectangular dissection graph
Notes: For example, this one is an octal rectangular dissection graph represented this rectangular dissection.
This cell corresponds to this node, …

## Slide 16
Unify-Cells (Unification of vertically adjacent cells)
d
c
e
Operations of cells
Vc Vd Ve
16
Unify-cell provides the unification of two cells c and d
Input Output
D E
GD GE
GD=(VD,ED,L,λD,A,αD) GE=(VE,EE,L,λE,A,αE)
Notes: As a simple of operations on cells, let me show you the algorithm called “Unify-Cell”.
Unify-cell provides the unification of two cells c and d by reducing a vertex and change edges like this.

## Slide 17
3. Landform
Octal Graph
17
Notes: Let me show you our results.
The first result is concerned with the landform octal graph.

## Slide 18
3.1 Landform Octal Graph
D = (T, P, g) : a rectangular dissection A Landform Octal Graph GD=(V, E, L, λ, A, α) for D is defined similarly to an octal degree rectangular dissection graph, where
A = { nw, sw, ew, ww, altitude, geological information, ..} α : V → A
3D landform map D G
18
Notes: The landform octal graph is defined as follows.
The altitudes in these red circles on this 3dlm are stored in these cells.
We note that the perimeter cells of the rectangular dissection are not displayed in this 3dlm.
We therefore defined the attribute function, α , from the set of vertexes, V, to the set of attributes, A.
The attribute set A includes altitude and other geological and geographical information at each point as well as the positions of walls.

## Slide 19
3.2 Example of Landform Octal Graphs
A 3D Landform Map
The Corresponding
Rectangular Dissection
The Corresponding
Landform
Octal
Graph
19
Notes: This picture is a sample of 3D landform map.
And these are a corresponding rectangular dissection and landform octal graph respectively.
or
These pictures are the 3Dlm and corresponding rectangular dissection and corresponding to log.

## Slide 20
Unification of two adjacent cells
Rectangular
Duals
Octal
rectangular
dissection
Graphs
the number of edge form one vertex is at most 8.
Using Unify-Cell, landform octal graph representation may reduce the number of polygons in focused area in shorter computation time than rectangular duals’s one.
3.3 Characteristics of Landform Octal Graph
n: number of
cells
20
O(1)
O(n)
Notes: I will now discuss the characteristics of the landform octal graph.
Let’s look at differences in the computation time for unify cells.
This n is the number of cells.
In the case of rectangular dual,
the computation time is proportional to n,
Because the number of edges form one vertex is also proportional to the number of adjacent cells.
But, in the case of the octal graph, the computation time does not depends on n.
Because the number of edge form one vertex is at most 8.
Accordingly, using Unify-Cell, landform octal graph representation may reduce the number of polygons in focused area in shorten computation time than rectangular duals.

## Slide 21
4. Implementation of
Landform Octal Graph
21
Notes: The second result concerns with the implementation of the landform octal graph

## Slide 22
H7-Code
1. header block
2. list block
3. content block
4. Tabular layer block
4.1 H7-Code : List structure for
implementation of
Landform Octal Graph
H7-code is based on heterogeneous
rectangular code called H3-Code.
H7-Code Consists of four blocks.
22
Notes: H7-code is the list structure to make the octal graph.
It is based on heterogeneous rectangular dissection code [3] called the H3-code and consists of four 4 blocks.
The first block is named the header block, which has information about the version of the H7-code.
The second block is named the list block, which stores the attributes of nodes,. their color, and their altitude.
The third block is named the content block, which contains the texture of 3D landform maps.
The fourth block is named the tabular layer block, which has information for management of plural H7-code files.

## Slide 23
4.2 Contents of list block
altitude
Landform Octal graph
Corresponding list structure
H7-Code.
Fields of each record
23
Notes: These pictures are the log and corresponding list structure, and details on one list block.

## Slide 24
4.3 Example of H7-Code file
# This file was transformed by map2h7-50m Version 1.14
# Date: 2005.08.31 Time: 17:13
# MESH SIZE: 50m
# MAP NAME:Mt. FUJI
# MESH CODE: 533805
# LINE: 001 - 200 (ORG: 001 - 200)
# COLUMN: 001 - 200 (ORG: 001 - 200)
1.14 200 200 0 0 0 0 0
1 0 0 0 2 0 0 203 0 203 0 1 -1 0 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
2 0 3 1 3 1 0 204 0 204 0 1 0 0 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
3 0 4 2 4 2 0 205 0 205 0 1 1 2 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
4 0 5 3 5 3 0 206 0 206 0 1 2 3 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
5 0 6 4 6 4 0 207 0 207 0 1 3 4 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
6 0 7 5 7 5 0 208 0 208 0 1 4 5 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
7 0 8 6 8 6 0 209 0 209 0 1 5 6 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
8 0 9 7 9 7 0 210 0 210 0 1 6 7 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
9 0 10 8 10 8 0 211 0 211 0 1 7 8 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
10 0 11 9 11 9 0 212 0 212 0 1 8 9 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
11 0 12 10 12 10 0 213 0 213 0 1 9 10 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
12 0 13 11 13 11 0 214 0 214 0 1 10 11 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
13 0 14 12 14 12 0 215 0 215 0 1 11 12 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
14 0 15 13 15 13 0 216 0 216 0 1 12 13 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
15 0 16 14 16 14 0 217 0 217 0 1 13 14 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
16 0 17 15 17 15 0 218 0 218 0 1 14 15 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
17 0 18 16 18 16 0 219 0 219 0 1 15 16 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
18 0 19 17 19 17 0 220 0 220 0 1 16 17 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
19 0 20 18 20 18 0 221 0 221 0 1 17 18 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0 0 0
20 0 21 19 21 19 0 222 0 222 0 1 18 19 0 0 0 0 0 0 0 0 0 0 -1 0 0 0 0 0
. . .
H7-code to represent a small part of Mt. Fuji land form map
Mt. FUJI
24
Notes: This is a picture of Mt. Fuji produced form this a H7-code file.

## Slide 25
4.4 Implementation: Structure of 3D Landform Map System
Altitude Data
H7-Code generator
N2H7
H7-Code
H7-Code
Transformer
VRML generator
H72V
VRML
25
VRML
Rendering
H7-code are converted into vrml.
Altitude data are converted into H7-code.
We reduce the number of cells.
Notes: The H7-code generator produces H7-code files from numerical attribute data.
We reduced the number of cells in 3dlm by composing H7-code files here.
Moreover, H7-Codes are converted into vrml files, which can be browsed through a Web browser and with VRML plug-ins.

## Slide 26
26
5. Comparison with Known Data Structure
Notes: Let me show you advantages of our new data structure.
To do this, we need to compare the number of meshes reduced quadtree with that by log.

## Slide 27
Problem
Input :
1km resolution altitude data of 16km x 16km specified meshed area
Output :
rough resolution altitude data of same area
Condition :
Adjacent cells c and d with their horizontal (vertical) walls in common are possibly unified if the difference of altitude of c and d is less than specified difference (threshold value) of altitude
Notes: We set problem.
As for Input , 1km resolution altitude data of 16km x 16km specified meshed area.
As for Output, rough resolution altitude data of same area.
Condition : Adjacent cells c and d with their horizontal (vertical) walls in common are possibly unified if the difference of altitude of c and d is less than specified difference (threshold value) of altitude

## Slide 28
Example
  Input area : NAGANO area in Japan, 16 x 16 cells
  Threshold Value : 10 m output
  input
  Output
    Quad tree case 55 cells
    landform octal graph case 27 cells
  Assertion
  Octal graphs possibly decrease cells more than quad trees
Quadtree
Landform
Octal
Graph
Notes: Example for.
Input area : NAGANO area in Japan, 16 x 16 cells.
Threshold Value is 1km.
As Output,
In the case of Quad tree is 55 cells.
In the case of landform octal graph is 27 cells.
Therefore, Octal graphs possibly decrease cells more than quad trees.

## Slide 29
6. conclusion
1. We proposed octal graph representation for multi-resolution 3D landform maps:
・Landform octal graph: octal graph
+ altitude + color
2. We implemented a landform octal graph with H7-code.
3. We proposed 3D Landform Map System
4. Advantage of landform octal graph over quadtree.
Future works
1. Implementation of 3D Landform Maps System
2. Extension to hexadecimal graph representation for stratum maps
29
Notes: We proposed octal graph representation for multi-resolution 3D landform maps. A landform octal graph is composed of an octal graph, altitude, and color. We implemented a landform octal graph with H7-code. We also proposed a structure for a 3D landform map system and discussed the advantages of the landform octal graph over quadtree.
As Future work,
We plan to implement a structure for a 3D landform map system in the future and extend to hexadecimal graph representation for stratum maps.

## Slide 30
Thank you!!
Notes: Thank you very much for your kind attention.

## Slide 34
Quadtree Vs Landform Octal Graph
Unify Cells
(if complementary 0～10, than Unify cells)
Nagano Landform data
Number of cell : 64
Quadtree
Landform
Octal
Graph
27
Notes: We compare landform octal graph with quadtree to
confirm in advantage of landform octal graph.
We make rectangular dissection of Nagano's
altitude data, confirm Unify cell of several method.
Left up rectangular dissection be made method of
quadtree.
Right down rectangular dissection be made
method of landform octal graph.

## Slide 35
Quadtree Landform Octal Graph
Number of cell : 55 Number of cell : 27
Number of cell : 64
We show advantages of landform octal graph by the number of cells.
28
Notes: Number of cell of original rectangular dissection is
64.
Number of cell of rectangular dissection to be
made method of quadtree is 55.
Number of cell of rectangular dissection to be
made method of landform octal graph is 27.
therefore we show to reduce number of cell
by method of landform octal graph than quadtree.
We show advantages of landform octal graph by
the number of celsl.

## Slide 36
Altitude Data
H7-Code
Transformer
H7-Code
Composer
H7-Code
H7-Code
4.5 Example: 3D Landform Viewing with Sloution change based on H7-Code
Notes: H7-code transformer transform from Attribute
data to H7-code files.
So to reduce cell H7-code operate.
At Rest Last picture.

## Slide 37
Apply Octal Graph to 3D Landform Maps,we make the system of rendering and transformation of 3D Landform Maps composed heterogeneous rectangular dissection.
1.4 Our GOAL
Notes: goal of our works.
Apply Octal Graph to 3D Landform Maps, we make the system of rendering and transformation of 3D Landform Maps composed heterogeneous rectangular dissection.

## Slide 38
4.3 ヘッダー部、リスト部
(1) ヘッダー部 header block
表の基本情報，３つのフィールドからなる
（予備フィールドを除く）．
Information of tabuer .constracted 3 field
(2) リスト部 list block
表のセルの情報を表す．
セルの数と等しい数のレコードからなる．
１レコード当たり32フィールド．
各フィールドはセル同士のリンク情報や地理情報（標高など）を持つ．
Information for cell of tabular.
32 field for 1 record.
Notes: Header block is
list block is

## Slide 39
4.4 コンテンツ部、表レイヤー部
(3) コンテンツ部 content block
各ノードに付随する，地名，画像（地図）
などの情報を格納．
1コンテンツ当たり8つのフィールドからなる
（予備フィールドを除く）．
Constract name of ,picture
(4) 表レイヤー部 tabular reyer block
複数の表を管理するための情報．
Information for control tabulares.
Notes: Content block and tabular reiyer block.
Content block is
tabular reiyer block is

## Slide 40
3.4 既存の手法との比較
QUADTREE
(4分木)
Rectangular Dual
(双対グラフ)
この4分木のままでは、
この部分の合併は対象外
合併の計算時間はO(n)
ｎはセルの数

## Slide 41
3D地形図表示ソフトの一例
Google Earth

## Slide 42
1.2.1 QuadTree
1. Introdution
It is

## Slide 43
矩形分割の記述
風車の記述は不可能
1. Introdution
1.2.1 Character of QuadTree

## Slide 44
1.2 BACKGROUND
QuadTree ( Bentley, 1975 )
Rectangular Dissection
Unifies two adjacent inner cells in a rectangular dissection.
1. Introdution

## Slide 45
1.2 BACKGROUND
1.2 BACKGROUND
Rectangular Dual ( kozminski & kinne.1985 )
Rectangular Dissection
特徴
1. Introdution

## Slide 46
1.2 BACKGROUND
1.2 BACKGROUND
Rectangular Dual ( kozminski & kinne.1985 )
Rectangular Dissection
記述全部可能
矩形分割の記述
1. Introdution

## Slide 47
1.2 BACKGROUND
1.2 BACKGROUND
Rectangular Dual ( kozminski & kinne.1985 )
Rectangular Dissection
Unifies two adjacent inner cells in a rectangular dissection.
全て可能.
計算時間はO(n)
ｎはセルの数
1. Introdution

## Slide 48
1.2 BACKGROUND
1.2 BACKGROUND
Octal Degree Rectangular Dissection Graph
( Motohashi el.2003 ), 今回利用
Rectangular Dissection
特徴
1. Introdution

## Slide 49
1.2 BACKGROUND
1.2 BACKGROUND
Octal Degree Rectangular Dissection Graph
( Motohashi el.2003 ), 今回利用
Rectangular Dissection
記述全部可能
矩形分割の記述
1. Introdution

## Slide 50
1.2 BACKGROUND
1.2 BACKGROUND
Octal Degree Rectangular Dissection Graph
( Motohashi el.2003 ), 今回利用
Rectangular Dissection
全て可能
計算時間はO(1)
Unifies two adjacent inner cells in a rectangular dissection.
1. Introdution

## Slide 51
2.1 3D Landform Maps
地形図
く
対応する矩形分割

## Slide 52
矩形分割 D
8分グラフの定義のつづき
（αDの説明）
GD=｛VD、ED、LD、λD、AD、αD｝
VD＝｛頂点の集合｝
LD＝｛辺のラベル全体：
enw, esw, eew, eww｝
ED＝｛辺の集合｝
αD：セルの位置・大きさ
を決める関数
｛nw, sw, ew, ww｝
c
ew(c)
ww(c)
nw(c)
sw(c)
2.2 Octal Graph

## Slide 53
矩形分割 D
定義 8分グラフ
VD＝｛頂点の集合｝
ED＝｛辺の集合｝
eww
eew
esw
esw
enw
2.2 Octal Graph [2]
（注）8分グラフの各頂点から出る辺の数は高々8本である
c

## Slide 54
４分木の手法によるセルの合併：
（1）異なるブロック位置のセルの合併／分割は対象外
1. 4.1 Example 1
1. Introdution

## Slide 55
双対グラフの手法によるセルの合併の計算時間：
（2）下の赤いセルの合併の計算時間はO(n)
1. 4.1 Example 2
1. Introdution

## Slide 56
(1) 多重解像度，および，その動的変化に対応した
データ構造の提案．
Compose Multi-Resolution, and data Structure relative motion
transformation.
(2) 提案したデータ構造を応用した多重解像度3D地形図 の生成・表示システムの概念モデルの提案．
Compose model for the system of renderring and transformation of 3D Landform Maps applied data structure.
1.6 Purpose
1. Introdution

## Slide 57
3.3 地形8分グラフの特徴
(1) 4分木では表現する矩形分割に制約があるが， 地形8分グラフではその制約がない．

## Slide 58
(1B) そのような地形8分グラフ表現の実装のために，H7-Codeと呼ばれるリスト構造を導入
(2) 3D地形図生成・表示システムの概念モデルの
データ流れ図
make data flow for model of renderring and transformation
of 3D Landform Maps
目的2:提案したデータ構造を応用した多重解像度3D地形図
の生成・表示システムの概念モデルの提案
Compose model for the system of renderring and transformation of 3D Landform Maps applied data structure.
．